5. DESCRIPTION OF FUSES

Figure 3

3. INSTALLATION DIAGRAM

Figure 1

J1 - manipulator socket, telephone plug 6p6c,

J2 - socket for peripheral devices, telephone plug 6p6c,

J3 - horn handling socket, loudspeakers, radio, additional, (pins 11 and 12 - pointing to minus),

J4 - power socket of the central unit,

J5 - power socket for warning lights,

J6 - control socket for warning lamps: 1 - channel and blue lamps, 3 - channel II blue lamps, 5 - channel III red lamps, 2, 4, 6 - channels of additional lamps F1, F2, F3,

Use cables min. 1.5mm2, use a shielded cable for connecting the radio.

J3, J4, J5, J6 - Mini-Fit 13A plugs

4. FUNCTION DESCRIPTION

Figure 2

"Turn on the generator" button - activates the active standby of the generator, resetting all settings to basic. When the generator is turned off, the light stays on.

"Turn off generator" button - when warning sounds are not generated,

it turns off the whole device. When a warning sound is emitted,

pressing only turns off warning sounds.

The button "turn on radio broadcast" - starts broadcasting messages from the radio or other device, blanks off the lights, leaving the radio keys illuminated, vol + and vol- and the LED indicator. When a warning sound is emitted, it will be muted until the broadcast function is turned off.

PTT "turn on microphone" button - when a warning sound is not heard, it starts broadcasting messages from the microphone. When a warning sound is emitted, it will be muted until the microphone function is turned off.

Button "increase volume" - increases the volume of broadcasting messages from the radio or microphone, signaling it on the LED indicator. The function is active only when activating the microphone or broadcasting from the radio.

"Decrease volume" button - decreases the volume of broadcasting messages from the radio or microphone, signaling it on the LED indicator. The function is active only when activating the microphone or broadcasting from the radio.

"On/off modulation" button - pressing the button results in the commencement of sounding of warning signals with simultaneous switching of blue warning lamps. Pressing again results in turning off the generation of warning beeps, leaving the blue lights on.

"Modulation change" button - pressing the button results in changing the emitted modulation according to the order: wail → yelp → priority → hi-lo → wail, etc.

"Airhorn" button - pressing the button results in the sound being emitted

the so-called. "Airhorn." Releasing interrupts the sound emission.

Button "turn on 1 channel of blue lamps" - pressing the button results in activation of 1 and 2 channel of warning lamps or 1 channel of blue lamps and channel responsible for changing the color of the lamp (in the case of blue-orange lamps). The next press switches off channel 1, 2 and if it is switched on - 3 channels of red lamps.

Button "turn on 3 channel of red lamps" - pressing results in starting the channel 3 red in warning lamps and 1 and 2 blue lamps. The next click will turn off the red warning lights.

Button "turn on 2 channel of blue lamps" or "turn on blue lamps when two-color lamps are used" - pressing results in switching on channel 1 and 2 of blue lamps or 1 channel of blue lamps and starting channel responsible for the color of light (blue). The next press (turn off) results in turning off the 2 channel of blue lamps or changing the color of the emitted light into orange.

Button "turn on 1 channel of additional lamps" - pressing results in switching on channel 1 of additional lamps. The next press results in the channel being turned off.

Button "turn on 2 channel of additional lamps" - pressing results in switching on channel 2 of additional lamps. The next press results in the channel being turned off.

Button "turn on 3 channel of additional lamps" - pressing results in switching on the channel of 3 additional lamps. The next press results in the channel being turned off.

LED indicator - indicates the volume level of the microphone or radio.

Microphone - allows you to make voice messages.